## Slide 1
Presented by
Md. Ruhul Amin
Warehouse Inspector
Office of Assistant Director, Dhaka
Search & Rescue During Structural Fire

## Slide 2: Contents
Elementary Equipment Needed for Search and Rescue
FBI – Fire Behavior Indicators
Smoke Reading
Sar Concept/Strategies/Tactic

## Slide 3: Elementary Equipment Needed for Search and Rescue
Full personal protective clothing
Self contained breathing apparatus
Radio, forcible entry tool, flashlight
A Partner
Hose line or a safety rope to entry/exit door

## Slide 4
To avoid unwanted fatalities, injuries of firefighters due to rapid fire progress during SAR in structural fire.
Be aware of structural vulnerability
FBI – FIRE BEHAVIOR INDICATORS
BSHAF

## Slide 5
Building construction influences both fire development and potential for collapse.
Occupancy and related contents will have a major impact fire dynamics. (Consider fire behavior during pre-incident planning.)
Elements to consider: Construction, Contents, Size, Ventilation Profile & Fire Protection Systems.
Structural, Nonstructural, Partition wall (load bearing/non load bearing) Fire resistive/non fire resistive
Residential/Industrial/Commercial/ Mix occupancy/Educational/ Health facilities Stored combustible materials
Interior/Exterior Finishing Materials Ventialtion Factor (Design/Natural/Mechanical)
B – BUILDING

## Slide 6
Building construction influences both fire development and potential for collapse.
Occupancy and related contents will have a major impact fire dynamics. (Consider fire behavior during pre-incident planning.)
Elements to consider: Construction, Contents, Size, Ventilation Profile & Fire Protection Systems.
Structural, Nonstructural, Partition wall (load bearing/non load bearing) Fire resistive/non fire resistive
Residential/Industrial/Commercial/ Mix occupancy/Educational/ Health facilities Stored combustible materials
Interior/Exterior Finishing Materials Ventialtion Factor (Design/Natural/Mechanical)
B – BUILDING

## Slide 7
Building construction influences both fire development and potential for collapse.
Occupancy and related contents will have a major impact fire dynamics. (Consider fire behavior during pre-incident planning.)
Elements to consider: Construction, Contents, Size, Ventilation Profile & Fire Protection Systems.
Structural, Nonstructural, Partition wall (load bearing/non load bearing) Fire resistive/non fire resistive
Residential/Industrial/Commercial/ Mix occupancy/Educational/ Health facilities Stored combustible materials
Interior/Exterior Finishing Materials Ventialtion Factor (Design/Natural/Mechanical)
B – BUILDING

## Slide 9: Fire Growth & impact on Structure & construction material

## Slide 10: Fire Growth & impact on Structure & construction material

## Slide 11: Fire Growth & impact on Structure & construction material

## Slide 12: Fire Growth & impact on Structure & construction material

## Slide 13: Fire Growth & impact on Structure & construction material

## Slide 14: Fire Growth & impact on Structure & construction material

## Slide 15: Fire Growth & impact on Structure & construction material

## Slide 16: S – SMOKE
Extremely useful in determining fire location and extent.
Smoke indicators may be visible on the exterior as well as inside the building.
Reading the smoke is critical, but not sufficient in predicting fire behavior.
Elements to consider: Location, Optical Density (Thickness), Color, Physical Density (Buoyancy), Volume.

## Slide 17: Buoyancy Induced Smoke Movement
https://www.youtube.com/watch?v=cLBtRwJ93aQ

## Slide 18: A – AIR TRACK
Air track includes movement of both smoke and air.
Observation of air track:
  Starts from the exterior
  Becomes more critical when making entry.
  Continues to be important while working inside.
Elements to consider:
  Direction, Wind, Velocity & Flow

## Slide 19: H – HEAT
Heat and temperature cannot be directly observed:
  Indirect indicators
  Tactile indicators
Protective clothing provides insulation,
Temperature changes faster than we feel it!

## Slide 20: H – HEAT

## Slide 21: F – FLAME
Flames may be obvious, but these indicators must be integrated with the other B-SAHF indicators.
Elements to consider: Location, Size, Color, Duration, Auto-ignition

## Slide 22
Determining the four key attributes of smoke
Smoke Reading
Notes: Shimmering ঝলমলে

## Slide 23
In what ways are they changing?
How rapidly are these changes occurring?
What do these changes suggest about the progression of the fire?
Two triggers: right temperature, right mixture
Smoke Reading

## Slide 24
-Remove endangered occupants
-Control The Fire
-Rmove Smoke & Toxic Gases
-Rescue
-Confine/Extingusih
-Natural/Tactical Ventilation
-Conduct Primary Search
-Place hose lines inside to control the fire
-Ventilate the building horizontally/vertically
Objectives | Strategies | Tactics
SAR concept/Strategies/Tactic

## Slide 25
-Remove endangered occupants
-Control The Fire
-Rmove Smoke & Toxic Gases
-Rescue
-Confine/Extingusih
-Natural/Tactical Ventilation
-Conduct Primary Search
-Place hose lines inside to control the fire
-Ventilate the building horizontally/vertically
Objectives | Strategies | Tactics
SAR concept/Strategies/Tactic

## Slide 26
-Remove endangered occupants
-Control The Fire
-Rmove Smoke & Toxic Gases
-Rescue
-Confine/Extingusih
-Natural/Tactical Ventilation
-Conduct Primary Search
-Place hose lines inside to control the fire
-Ventilate the building horizontally/vertically
Objectives | Strategies | Tactics
SAR concept/Strategies/Tactic

## Slide 27
Phase of Search & Rescue:
Primary Search
  • Early action
  • Fast movement
  • Victims can be seen
  • No other activities
SAR in Structure

## Slide 28: Priority of Rescue

## Slide 29
ii. Secondary Search
  • Fast movement
  • Search victims (can’t see victims)
  • Victims hide/trap
  • Use equipments (SCBA, hose, mechanical ventilation etc.)
SAR in Structure

## Slide 30: Entry into a structure
Get down low, check door for heat, open door and check flooring
Enter Structure and perform either a right or a left and search
At least once a room Yell (Fire Department is anyone in here)
Always STAY TOGETHER

## Slide 31: As Entering
First person deciminate through radios that team is entering and give the name of the team and the direction of search to the commander.
Second person is to grab the outer boot of first rescuer and search with a tool in the other hand as far as he can reach.
Third Person is to do the same as second rescuer except to hold onto the second mans outer boot

## Slide 32: During Search
Always keep the team informed of what you are finding. (windows, doors, closets)
Always be aware of your partner(s)
Feel the walls for windows or secondary egress routes.
Search all areas (Toilets, under beds/tables Etc.)
Ventilate when possible taking care not to give the fire air

## Slide 33: Small area search technique
First person enters while second holds doorway.
Then second enters while third holds doorway.
Speeds up the process of the search.

## Slide 34: Large area search Technique
In larger rooms you can use webbing or a short rope to keep contact with your team.
You could hold hands.
Using these during a search can extend your search area further into a room to get a full and accurate sweep.

## Slide 35: Finding Victim
Radio command of whereabouts of the victim and status of the victim to get EMS teams ready.
Leave a tool or something to mark your end of search so the next team can take over.
During exit time, explain to next team all about your search so they have your information to make their search

## Slide 36: After exiting the Building
Always put your tools in a proper staging area, or put it back in its place in service.
Extend your air pack straps, check it over, clean it, fill the air tank, put in back in a staging area or in its place on the truck.
Go to rehab

## Slide 37: Structural collapse all call
Whenever anyone finds a structural problem alert the commander of it.
If the commander sees bad sign he will call all personnel out of the building by the use of his radio and the use of an air horn/ whistle on a truck.
It consists of three blasts of the air horns three times as well as a radio message to immediately egress out of the building.

## Slide 38: Structural collapse all call
https://www.youtube.com/watch?v=bN2O_k7QJlY

## Slide 39: Things to be remembered
Do the best job you can with the resources you have.
Search thoroughly
Take care of you and your team FIRST.
Stay low and together
Always use a hose line or a rope to the exit when you search.
Always take care of yourself and your partners.
We are called to be a solution to, not to add to the problem.
YOU are the most important person on any scene!
Remember: practice does not make perfect. PERFECT PRACTICE MAKES PERFECT!!!

## Slide 42: Potential energy convert to Kinetic energy and light
https://www.youtube.com/watch?v=eocyl9dZ7W0